## Slide 1: The Impact of Self-consumption Regulation on Individual and Community Solar PV Adoption in Switzerland: an Agent-Based Model
Master Thesis Final Presentation
Prakhar Mehta, MEST
Supervisors: Danielle Griego, Alejandro Nuñez-Jimenez
Examiner: Professor Dr. Arno Schlüter

## Slide 2: Agenda
Introduction and Motivation
Data and Methodology
Results
Conclusion and Discussion

## Slide 3
Notes: Tremors around the world – govt act

## Slide 4: The Energy Transition
11.4 TWh
PV
1.6 GW  7 GW
1.4 TWh
20 TWh
2017
2035

## Slide 5: Helpful New Regulations – Energy Act 2018
EWZ Factsheet Solarsplit
Investment Subsidy until 2030: up to 30% investment costs
for 2 kW – 50 MW PV Systems
FiT: 7.91 Rp./kWh
Zusammenschluss für Eigenverbrauch (ZEV) Formation
Self-consumption Communities
Restrictions:
Can’t share across public property, roads, other private properties
Buildings must be adjacent, common grid connection
Notes:   Typical 3-4 person household = 3500 – 4500 kWh per year = 3-4 kW PV enough
  Mandatory for EWZ: FiT = 7.91Rp./kWh in Zurich
  Only one-time subsidy from government: up to 30% of PV system costs
  Multiple  Single customer
  Building Owner/Tenants  form ZEV, share system costs and electricity in premises
  Idea is to not put extra electricituy into the grid

## Slide 6: ZEV = Community Solar!
Community PV Systems
Economies of Scale
Complementary Load Profiles
Financial Benefits/Products
Notes: Not just one bldg. – multiple come together
Community solar definition -
Great case for community solar
Complementary building types closely packed together
Alt-Wiedikon: high resolution CEA data

## Slide 7: Problem Statement
How will the dynamics of future solar PV adoption evolve in urban Switzerland, given the new regulations which incentivize individual solar PV adoption even more than before, and allow the formation of self-consumption communities?
Will community PV adoption outpace individual PV adoption?
What potential policy implications and problems can be foreseen?
Notes: Need for solar and new regulations in place

## Slide 8: Objectives
Use of regulations to form potential communities in Zurich
Develop a decision-making methodology for solar PV adoption – individual and community
Explore the dynamics of individual and community solar PV adoption under the new regulations for the period 2018-2035 in the district of Alt-Wiedikon, Zurich.
  Scenarios
Notes:   Research Questions
  Will the adoption of community scale solar PV outpace individually owned solar in the Swiss urban context, given current regulations?
  What elements of the current regulation have greater impact on adoption levels?
    Level of subsidies
    Size of allowed communities

## Slide 9: Agenda
Introduction and Motivation
Data and Methodology
Results
Conclusion and Discussion

## Slide 10: Alt-Wiedikon Buildings Distribution
6856 Buildings 13 Typologies
73% Residential/Mixed-use Residential
Notes: Diff bldg. types and age

## Slide 11: Aggregation of Buildings
14 buildings
1 building block

## Slide 12: Alt-Wiedikon Buildings to Building Blocks
6856 Buildings  1950 Building Blocks
13 Typologies
3 Typologies
73.27%
20.25%
6.47%
Notes: Diff bldg. types and age

## Slide 13: Making Plots in Alt-Wiedikon - OSM
406 Plots
Notes: Diff bldg. types and age

## Slide 14: Making Plots in Alt-Wiedikon - OSM
117 Plots – only one building block!
= no Community PV option
406 Plots
Notes: Those are still building blocks! Many individual buildings

## Slide 15: Potential ZEV Members – example of a Plot
Number of Possible ZEVs for A: 15
A +B + C + D + E
A +B + C + D
A +B + C + E
A +B + D + E
A +B + C + E
…
A + B …
A | B | C | D
B | A | A | A
C | … | D | C
D | … | … | …
E | … | … | …
B
A
C
D
E
Notes: Radius taken for the buildings
In reality these are ZEVs as they are multiple buildings

## Slide 16: Agent-based Modelling

## Slide 17: Emergent Phenomena
“Solar PV is Eco-friendly, Easy…”
“I cannot afford solar PV”
“Climate Change is a conspiracy!”
“My friends think PV is cool”

## Slide 18: The Theory of Planned Behaviour
“Solar PV is Eco-friendly, Easy…”
“My friends think PV is cool”
“I cannot afford solar PV”
Icek Ajzen, ‘Constructing a TPB Questionnaire: Conceptual and Methodological Considerations’, 2002

## Slide 19: Use of TPB for decision making: Stage I – Idea Generation
IDEA Generation
Do I want solar?
Yes/No
Variables
Environmental attitude: [0,1]
+
Small-world Network : [0,1]
Ratio:
Neighbour Persuasion:
Economic Attractiveness : [0,1]
Profitability Index =1 +
Notes: TPB has 2 stages – intention, and behaviour
Subjective norms – what does society think
PBC - Does agent feel confident enough to do it?
PP = how quickly does the investment pay off compared to other investments
Need to quantify these qualitative ideas
First, let us try to quantify the intention, Forget about the behaviour for now

## Slide 20: Use of TPB for decision making: Stage II – Behaviour
Variables
Environmental attitude : [0,1]
+
Small-world Network : [0,1]
Ratio:
Neighbour Persuasion:
Economic Attractiveness : [0,1]
Profitability Index =1 +
Choice:
Individual OR Community based on NPV
Notes: TPB has 2 stages – intention, and behaviour
Subjective norms – what does society think
PBC - Does agent feel confident enough to do it?
PP = how quickly does the investment pay off compared to other investments
Need to quantify these qualitative ideas
First, let us try to quantify the intention, Forget about the behaviour for now

## Slide 21: Flowchart Decision-Making

## Slide 23: Scenarios
Model A – Reduced (~ half the population)
716 building blocks < 100 MWh
Retail Prices
Compensates for CEA Building Aggregation
2 Cases:
  No-ZEV  no community solar. Used for calibration
  ZEV  communities allowed < 100 MWh. Compare with no-ZEV.
Model B – Alt-Wiedikon
1437 building blocks – entire district
ZEV 2 Cases:
  Retail Prices
  Wholesale Prices
Electricity Prices –
  Retail (< 100 MWh annual demand): 24.3 - 14.4 Rp./kWh
  Wholesale (> 100 MWh): 6 - 5 Rp./kWh
Unclear if building owners purchase on wholesale markets

## Slide 24: Assumptions
Buildings  Building Blocks
  PV Sizes = Max Rooftop Sizes, else
  Building Block Sizes quite large = demands large = PV systems large
   NPVs amazing!
  Building Block – Individual, >1 Building Block = Community  different in reality!
  Much fewer agents than reality – simpler decision making
  Cooperation costs – purely monetary indicators used
Decision making at only owner level: all tenants say YES to a ZEV
Model calibrated with projected historical trend, not validated
Over time:
  Constant – Population, Attitudes, peer network, electricity prices, Subsidies and FiTs, ZEV members
  Changing – PV Prices, NPVs, Peer Effects
Notes: Fixing sizes – computationally intensive otherwise

## Slide 25: Methodology Overview
CEA Model
Alt-Wiedikon, Zurich
ABM for
Building Owners
[Individual/Community Adoption]
CEA Output Data Processing
Results Visualisation
Other Inputs
Peer effects, environmental attitudes, agent locations and networks
Prices – PV and Electricity
Regulations – FiTs, Subsidies and ZEV formation
Building Data, Geometry, etc.
Adoption levels Individual v Community PV Systems
Parameters
Agent Categories based on building type and ownership
Time: Yearly time steps until 2035

## Slide 26: Agenda
Introduction and Motivation
Data and Methodology
Results
Conclusion and Discussion

## Slide 27: Model A – Reduced no-ZEV
Neighbour persuasion
Profitability index
attitude
intention
Peer effects
Avg = 6500 kWp
Peers adopted in 2025, 2026
Plot members have positive intention in 2027
Subsidies Stop
PV
Peer Effects
An example Agent’s Variables and Adoption
in 2027
Targets Exceeded 1.5 times!
Notes: 1.5 times projected
Calibration

## Slide 28: Model A – Reduced ZEV – Community allowed
Total Adoption ~ 2x trend
2026-2030: ~ 1000 kW/year
81% Individual
19% Community – only. And delayed.
Avg TOTAL = 8000 kWp
Individual = 6500 kWp
Community = 1500 kWp
Notes: 2times projected
Community
Levels
EGIDs

## Slide 29: Model A – Reduced ZEV – Community allowed
22 ZEVs
  50 buildings
113 Individual Adopters
Why did they not adopt community?
  40%: No other potential ZEV member crossed intention
  30%: The community size was exceeding 100 MWh
  30%: I’m alone in my plot
Chart: Adoption Numbers in a typical ABM Run
| Residential | Commercial | Public
Individual | 65 | 36 | 12
Community | 35 | 12 | 3
No Adoption | 426 | 95 | 32

## Slide 30: Model B – Alt-Wiedikon
Wholesale: 4 times cheaper electricity!
Retail
Expensive Electricity
Avg TOTAL = 48000 kWp
Avg Comm = 4000 kWp
Avg TOTAL = 4000 kWp
Notes: Trend of projected
Patterns similar – coherent models
Retail – big PVs, amazing prices  adopt solar!
Community takes time, agents do not cross intention together
Wholesale  only adopt post 2024 – prices fall, peer effects increase. Smaller PV systems install, not larger

## Slide 31: Agenda
Introduction and Motivation
Data and Methodology
Results
Conclusion and Discussion

## Slide 32: Conclusion: Key Learnings
Targets exceeded. Subsidies stop and so do the adoptions  PV Prices not falling enough to recover. Lower subsidy magnitude but extend.
Community Formation Difficult and depends on many factors simultaneously
  Big PVs – economies of scale don’t matter
  Decision-making process – too many things must fall into place for community PV
  Many buildings – not many options
Individual adoption i.e. Aggregated buildings == ZEVs!
Electricity price levels extremely important to estimate future adoptions
  Owners don’t know about wholesale markets?
  Lack of expertise?
What will most likely happen – average of Retail + Wholesale adoption levels
Notes: Model ZEV without solar

## Slide 33: Future Work – Discussion and Limitations
Consider individual buildings, not blocks
   even individual apartments! Better distinction between individual and community
Varying PV Sizes – consider optimal for all
Electrical Grid distribution level data – plot formation
  Vary plot sizes
Community formation through greater feedback in decision-making
  Agents convince others in the same year
Adoption Process: If community not possible, then possibly agents wait
Social/Individualistic nature of people can be important to consider
Memory for the agents
Surveys to gather data
Notes:   Environmental attitudes
  Peer networks
  Economic indicators most valued, discount rates and paybacks considered
  Electricity Purchase Options

## Slide 34: Personal Conclusions
Deciding how to model decision-making is DIFFICULT!
ABM can be very subjective
Mood Shift: I can see myself doing this for 4 years!

## Slide 35: Thank You! Time for questions and discussion! 
@ Danielle
& Alejandro
@ Profs and Teams - A/S and SusTec
@ Peers – positive peer effect 

## Slide 36: Back-up Slides

## Slide 37: Calibration - Model A
Weights | Value
Economic Attractiveness | 0.3
Peer effects | 0.35
Environmental Awareness | 0.35
Negative NPV allowed | YES -15% of Investment costs
Weights | Value
Economic Attractiveness | 0.31
Peer effects | 0.3
Environmental Awareness | 0.39
Negative NPV allowed | YES -5% of Investment costs
RMSE = 117
Notes: Negative NPV necessary to emulate adoptions
Maybe people consider long paybacks or low discount rates

## Slide 38: Model B – Alt-Wiedikon
Weights | Value
Economic Attractiveness | 0.31
Peer effects | 0.3
Environmental Awareness | 0.39
Negative NPV allowed | YES -5% of Investment costs
Weights | Value
Economic Attractiveness | 0.33
Peer effects | 0.42
Environmental Awareness | 0.25
Negative NPV allowed | NO

## Slide 39: My case: So. Many. Variables!
Environmental attitudes/beliefs Technical aspects
Economics
Past opinions
Individualistic/Social
Cost effectiveness
No. of installations in neighbourhood
Feedback based on peer decisions
What Peers Say
General Social Image of PV
Small-world Network (Closest people – Friends, Family)
Does agent feel confident enough to do it?
Money/Economic Attractiveness
Time
Skills
Support and Persuasion
Notes: What can be included in attitude toward the behaviour
What forms subjective norms
What forms PBC